## Slide 1
QUANTUM COMMUNICATIONS
Master Cybersécurité - Project Presentation Securing the Future of Telecommunications

## Slide 2
Context & Motivation
• RSA/ECC encryption vulnerable to quantum computers
• Q-Day may occur: 2030-2035 (uncertain but possible)
• Current encrypted data at risk: Harvest-Now-Decrypt-Later threat
• Solution: Quantum Key Distribution (QKD) + Post-Quantum Crypto (PQC)
• European leaders: ETSI standards + EuroQCI initiative
• Timeline critical: 2025-2027 deployment window

## Slide 3
Quantum Fundamentals: Superposition
Classical bit: 0 OR 1 (one state at a time)
Quantum bit (Qubit): |ψ⟩ = α|0⟩ + β|1⟩ (both states simultaneously)
Key property: Superposition exists UNTIL measurement
Measurement forces qubit to definite state (0 or 1)
Consequence: Observer cannot determine state without measuring
Cryptographic advantage: Eve's measurement attempt = detectable disturbance

## Slide 4
The No-Cloning Theorem
Fundamental principle: IMPOSSIBLE to copy unknown quantum state
Why relevant to cryptography:
✗ Spy cannot duplicate photon and send original unchanged
✗ Any espionage MUST involve measurement
✗ Measurement changes/destroys qubit state
✓ This change is DETECTABLE by legitimate parties
Core security guarantee: All eavesdropping attempts = discovered

## Slide 5
Quantum Entanglement (Bell States)
Two entangled photons share single indivisible quantum state
Example: |Φ⁺⟩ = (|00⟩ + |11⟩)/√2
Property: Measuring one photon instantly determines other
Non-locality: Correlation works even if photons far apart
Important: No information faster-than-light (respects relativity)
Used in: E91 protocol, MDI-QKD for enhanced security

## Slide 6
The Harvest-Now-Decrypt-Later Threat
TODAY (2024): Adversary collects encrypted data
• Intercepts TLS/RSA/ECC internet traffic
• Stores petabytes in secure vault
• Current encryption appears unbreakable
TOMORROW (2030-2035): Quantum computer becomes viable
• Shor's algorithm defeats RSA factorization
• Stored data suddenly becomes readable
IMPACT: Diplomatic secrets, medical records, financial data exposed

## Slide 7
Classical vs Quantum Security Comparison
RSA-2048 (Classical):
• Secure NOW: Yes (2^128 computational effort)
• Secure with Quantum Computer: NO ✗ (Shor's algorithm)
• Vulnerable from: ~2030-2035
QKD (Quantum):
• Secure NOW: Yes (unconditional, physics-based)
• Secure with Quantum Computer: YES ✓ (violates quantum mechanics)
• Vulnerable from: Never (protected forever)

## Slide 8
Recommended Defense Strategy (NIST/ETSI)
2024-2025: IMMEDIATE PHASE
• Deploy QKD for critical channels
• Evaluate Post-Quantum Cryptography (Kyber/Dilithium)
2025-2027: TRANSITION PHASE
• Hybrid: Use both QKD + PQC (defense in depth)
• Begin archiving sensitive >30Y data with QKD keys
2027-2030: CONSOLIDATION
• Post-quantum standard everywhere
• QKD specialized for ultra-sensitive data

## Slide 9
BB84 Protocol (Bennett-Brassard 1984)
First practical QKD protocol - still widely deployed
Goal: Securely distribute encryption keys
Process:
1. Alice: Generate random bits + random bases
2. Alice: Encode bits in photons using bases
3. Alice: Send photons to Bob over quantum channel
4. Bob: Measure photons with random bases

## Slide 10
BB84: Detailed Protocol Flow
SETUP: Alice generates
Bits: 0 1 0 0 1 1 0 1
Bases: + × + × × + × + (+ = rectilinear, × = diagonal)
TRANSMISSION: Alice sends 8 photons to Bob
BOB MEASURES:
His bases: × + + × + × + ×
Results: 1 1 0 0 1 ? 0 1 (? = wrong base = random)
SIFTING: Keep only positions where bases match
Final key: 0001 (50% of transmitted bits retained)

## Slide 11
Eavesdropping Detection in BB84
Eve attempts to intercept:
• Doesn't know Alice's bases (guesses 50%)
• When Eve guesses wrong: Qubit state CHANGES
• Bob receives corrupted photon
Detection via Quantum Bit Error Rate (QBER):
• No eavesdropping: QBER ≈ 1% (measurement noise)
• Complete eavesdropping: QBER ≈ 25%
• ETSI threshold: QBER > 11% → ABORT SESSION
Logical guarantee: No spy can escape undetected

## Slide 12
BB84 Security Properties
(+)Unconditional Security
Based on quantum physics laws, not math complexity
Remains secure even with quantum computers
(+)Eavesdropping Detection
Any spy caught with high probability
Uncertainty principle guarantees disturbance
(-)Authentication Required
Need secure channel for protocol messages
Currently RSA-based (2024-2026)
(-)Practical Limitations
Distance: ~100 km in fiber | Key rate: ~1 kbps

## Slide 13
Modern QKD Protocols: Evolution
DECOY-STATE QKD (Improves BB84):
• Problem: Real lasers emit multiple photons
• Solution: Mix real states + dummy 'decoy' states
• Benefit: Enables commercial laser sources (lower cost)
TWIN-FIELD QKD (TF-QKD):
• Problem: Distance limited ~100 km (fiber attenuation)
• Solution: Photons sent from both ends → interfere at midpoint
• Benefit: Distance 500+ km | Rate 4 Mbps (lab)
• Status: Cutting-edge research (2024-2026)

## Slide 14
QKD Protocols Comparison
BB84: Simple implementation | 100 km range | 1 kbps rate
→ Currently deployed in industry
E91: Entanglement-based | Same range | 0.1 kbps
→ Theoretical advantages, research focus
MDI-QKD: Device-independent | 200+ km | 0.01 kbps
→ Ultimate security, practical limitations
TF-QKD: Twin-field | 500+ km | 4 Mbps (lab)
→ Future production likely 2025-2027

## Slide 15
NIST PQC Standardization (2022)
Selected quantum-resistant algorithms:
ENCRYPTION (Key Encapsulation):
✓ CRYSTALS-Kyber - Lattice-based, practical
DIGITAL SIGNATURES:
✓ CRYSTALS-Dilithium - Lattice-based
✓ SPHINCS+ - Hash-based (conservative)
✓ FALCON - Ultra-compact lattice
Timeline: Migration 2025-2027 for critical systems

## Slide 16
Defense in Depth: QKD + PQC Integration
WHY BOTH?
• QKD = unconditional security (physics)
• PQC = post-quantum proof (mathematics)
HYBRID APPROACH:
Message encrypted: AES-256(K_combined)
K_combined = K_QKD ⊕ K_PQC
ADVANTAGES:
• QKD compromised? → PQC still protects
• PQC broken? → QKD still protects
• Better than relying on single mechanism

## Slide 17
QKD Network Topologies
POINT-TO-POINT:
Alice ↔ Bob | Simple but no scalability
STAR TOPOLOGY:
Central Hub ↔ Multiple nodes | Scalable, single point of failure
MESH TOPOLOGY:
All nodes interconnected | Robust, complex management
CURRENT DEPLOYMENT:
Most use Star (compromise 2024-2026)
Future: Transition to Mesh for critical infrastructure

## Slide 18
Transmission Channels: Fiber vs Space-Free
FIBER OPTIC (Terrestrial):
✓ Reuses telecom infrastructure
✓ 100 km range typical (attenuation 0.2 dB/km)
✓ Primary for urban/regional networks
SPACE-FREE (Satellite):
✓ Global coverage without physical infrastructure
✗ Weather dependent (clouds block signals)
✗ Low throughput (~100 bps from Micius satellite)
HYBRID (Best approach):
Fiber backbone for high-speed urban
Satellite bridges for long-distance/intercontinental

## Slide 19
Quantum Network Components
PHOTON SOURCE:
• Laser or entangled photon sources (SPDC)
• Produces quantum states for transmission
TRANSMISSION CHANNEL:
• Fiber optic (100 km typical)
• Attenuation: 50% loss per 5 km
DETECTOR:
• Single-Photon Avalanche Diodes (SPAD)
• Efficiency: 50-85%
• Dark noise: 100-10,000 counts/s
QUANTUM REPEATER (Future):
• Extends range to 500+ km | Status: Lab only (2024)

## Slide 20
Real-World QKD Deployments (2024)
EUROPE:
• Switzerland: Genève-CERN fiber network
• Netherlands: EuroQCI backbone planning
• Germany: Electricity grid pilots
ASIA:
• China: Jinan (10 nodes) + Micius satellite
• Japan: Tokyo metropolitan trials
NORTH AMERICA:
• USA: Chicago Quantum Exchange network
• Canada: Secure communications pilots
COMMERCIAL VENDORS: ID Quantique, Toshiba, Huawei

## Slide 21
Finance Sector: Banking Networks
WHY DEPLOY QKD:
• Transaction keys: 5-30 year confidentiality
• Customer data: 30-50 years (PII retention)
• Strategic secrets: 50+ years
REGULATION:
• Basel III: Secure communications mandatory
• Future: Post-quantum proof ~2027
DEPLOYMENT:
• SWIFT pilots (2023-2024): 10+ banks
• Production rollout: 2025+ planned
• Goal: 50% major banks by 2028

## Slide 22
Critical Infrastructure: Power Grid SCADA
CURRENT THREAT:
• Remote SCADA access via RDP/SSH
• Credential compromise = regional blackout
• RSA compromise = all sessions readable
QKD SOLUTION:
Commands encrypted: AES-256(K_QKD)
Re-key hourly | Any decryption = detected
DEPLOYMENTS:
• USA: NIST GridEx resilience tests
• Germany: Pre-deployment planning
• Japan: Post-Fukushima resilience initiative

## Slide 23
Healthcare: GDPR Data Protection
SENSITIVE DATA LIFECYCLE:
• Genetic information: 80+ years
• Mental health records: 80+ years
• Diagnoses: 30+ years
• Lifetime persistence in registries
GDPR EVOLUTION:
• Current (2024): Breach notification only
• Future (2027): Proof of 'adequate crypto' required
• Projected: QKD/PQC mandatory by 2029
IMPLEMENTATION: EHR encrypted AES-256(K_QKD)

## Slide 24
Practical Attacks & Side-Channels
DETECTOR BLINDNESS:
Eve sends intense photons → saturation
Eve sees all, Bob sees nothing
Fix: MDI-QKD (detector-independent)
TIMING ATTACKS:
Processing time varies by qubit state
Eve measures delay patterns
Fix: Constant-time randomization
ELECTROMAGNETIC SIDE-CHANNEL:
Power consumption reveals computation
Eve with nearby radio receiver
Fix: EM shielding + randomization

## Slide 25
Authentication Challenge: MITM Prevention
THE CIRCULAR DEPENDENCY:
QKD distributes secure keys
BUT QKD itself needs authentication
But authentication needs crypto... (circular!)
CURRENT SOLUTION (2024-2026):
• Pre-shared RSA certificates
• Out-of-band authentication (phone calls)
• Infrastructure network-level security
LONG-TERM FIX (2027+):
• Derive authentication keys from initial QKD
• Symmetric authentication (no PKI)

## Slide 26
Security Comparison: Q-Day Impact
CLASSICAL ENCRYPTION (RSA):
2024: SECURE ✓
2030: BROKEN ✗ (Q-Day, ~10M quantum qubits)
Data encrypted 2020-2024: Vulnerable NOW
QUANTUM KEY DISTRIBUTION:
2024: SECURE ✓ (physics-based)
2030: STILL SECURE ✓
2030+: STILL SECURE ✓ (forever)
WHY QKD SURVIVES:
Security = Physics (no-cloning law)
Quantum computers cannot violate no-cloning

## Slide 27
Technical Challenges & Solutions
DISTANCE PROBLEM:
• Fiber attenuation: 0.2 dB/km
• 100 km = only 1/5000 photons reach destination
• Solution: Quantum repeaters (for 500+ km)
THROUGHPUT PROBLEM:
• BB84: ~1 kbps maximum
• Finance needs: 1-100 kbps
• Solution: Twin-Field QKD (4 Mbps lab)
COST PROBLEM:
• 2024: €180K/km (boutique)
• 2028: €40K/km (moderate scale)
• 2030: €20K/km (commodity)

## Slide 28
Standards: ETSI, NIST, ISO
ETSI (European Telecommunications Standards):
✓ GS QKD 001-004 published | Architecture, security proofs
NIST (USA):
✓ PQC Standardization FIPS 203-205 (2022)
✓ Timeline: 2025-2027 adoption
ISO/IEC:
Quantum cryptography standards in development
✓ 30551 (QKD) | 23917 (PQC requirements)
GOAL: Convergence on 2-3 interoperable standards by 2026

## Slide 29
Global QKD Deployment Roadmap
2024-2025: INITIAL PHASE
Pilots: Banking, government | 10-20 cities | 50-100 km range
2025-2027: RAPID EXPANSION
Standards finalized | 100+ cities | Production repeaters viable
2027-2030: CONSOLIDATION (CRITICAL!)
Q-Day threat window opening
Archive re-encryption NOW or lose data protection
Hybrid QKD+PQC mandatory
2030-2035: MATURE
Continental QKD networks | Quantum computers real threat

## Slide 30
Recommended Strategy for France/EU (2024-2026)
IMMEDIATE ACTIONS:
• Budget: €50-100M for quantum research
• Deploy 2 urban QKD pilots (Paris-Lyon backbone)
• Lead ETSI standardization efforts
MEDIUM-TERM (2025-2027):
• National QKD strategy + PQC transition roadmap
• Train 5,000+ quantum engineers
• Archive sensitive data re-encryption program
BUDGET: €300-500M total (2024-2027)
COMPETITIVE DISADVANTAGE if delayed beyond 2025

## Slide 31
Key Takeaways
✓ Quantum computers will threaten RSA by 2030-2035
✓ Current encrypted data at lifetime risk without QKD/PQC
✓ BB84 QKD = unconditional security (physics-based)
✓ Eavesdropping = always detected (No-cloning theorem)
✓ Hybrid approach (QKD + PQC) = defense in depth
✓ 2025-2027 = critical deployment window
✓ Delay after 2027 = security debt + regulatory penalties

## Slide 32
Questions ?
Thank you for your attention! Presentation: Quantum Communications

## Slide 33
References
Bennett & Brassard (1984). Quantum cryptography: Public key distribution.
Ekert (1991). Quantum cryptography based on Bell's theorem.
Brunner et al. (2014). Bell nonlocality. Rev. Modern Physics, 86(2).
Scarani et al. (2009). The security of practical QKD. Rev. Modern Physics, 81(3).
ETSI (2020-2021). GS QKD 001-004 standards.
NIST (2022). Post-Quantum Cryptography Standardization: FIPS 203-205.
Quantum Internet Alliance: https://www.quantum-internet-alliance.org/